## Slide 1
NUCLEAR ENERGY BASICS,
PART 2:
REACTORS AND NUCLEAR FUEL MAKING
A presentation by Henry Sokolski Executive Director Nonproliferation Policy Education Center www.npolicy.org
© Nonproliferation Policy Education Center

## Slide 2: Questions to BE Addressed:
What are the basic stages of once-through uranium based fuel cycles?
What are the most popular methods of enriching uranium?
What are the different types of nuclear reactors and how proliferation prone is each?
What can be done with spent reactor nuclear fuel?

## Slide 3: Short Answers
There are six stages: Uranium mining and milling, conversion to uranium hexafluoride (UF6), uranium enrichment, fuel fabrication, generating nuclear electricity, spent fuel storage.
Centrifuges and gaseous diffusion
All types of reactors can make nuclear explosive plutonium– light water and heavy water reactors, gas cooled and graphite reactors, RMBK and fast reactors
Spent fuel can be recycled or not. In either case, there will be considerable waste that must be stored above or under ground.

## Slide 4: 0. Nuclear Fuel Cycle Basics

## Slide 5: There are two Major Paths to the Bomb

## Slide 6: U238 & U235: two important uranium isotopes
U238
Has 146 neutrons
constitutes 99.3% of uranium in nature
Is not prone to fission
U235
Has 143 neutrons
Constitutes .7% of uranium found in nature
Is prone to fission

## Slide 7: Uranium centrifuge enrichment separates the heavy uranium from the light uranium

## Slide 8: There are two Major Paths to the Bomb

## Slide 9: Uranium Transmutes to Plutonium in a Reactor

## Slide 10: Spent Reactor Fuel Contains Plutonium That Can Be Chemically Stripped Out (Reprocessed)

## Slide 11: 1. What are the basic stages of once-through uranium based fuel cycles?

## Slide 12: Once-Through Fuel Cycle doesn’t reprocess spent fuel
FIGURE 1

## Slide 13: Closed Plutonium-Based Fuel Cycle requires reprocessing
FIGURE 2

## Slide 14: Basic stages of once-through uranium-based fuel cycles
Uranium Mining and Milling
Conversion to Uranium Hexafluoride (UF6)
Uranium Enrichment
Fuel Fabrication
Generating Nuclear Electricity
Spent Fuel Storage

## Slide 15: Major uranium producers 2016
FIGURE 3

## Slide 16: Conventional uranium Mining
Underground
Open Pit

## Slide 17: In Situ Recovery mining method
1. Injection Wells
2. Recovery Wells
3. Monitoring Wells

## Slide 18: yellowcake

## Slide 19: Basic stages of once-through uranium-based fuel cycles
Uranium Mining and Milling
Conversion to Uranium Hexafluoride (UF6)
Uranium Enrichment
Fuel Fabrication
Generating Nuclear Electricity
Spent Fuel Storage

## Slide 20: UF4 (Green Salt) and uf6 (Uranium hexafluoride)

## Slide 21: Hexafluoride Conversion Facility– large & rare
Port Hope in Ontario, Canada

## Slide 22: Major hexafluoride uf6 producers
[t U/year] metric tons uranium/year

## Slide 23: 2. What are the most popular methods of enriching uranium?

## Slide 24: Most Countries that enrich uranium Use centrifuges
Gaseous Diffusion: Argentina
Centrifuge: Brazil, U.S.-URENCO, Holland, France, UK, Germany, Russia, China, Japan, Iran, India, Pakistan, North Korea

## Slide 25: The effort needed to enrich U to 3-5% is half of what is needed to enrich to Weapons-Grade u
Separative Work Units Needed to Enrich Uranium to Power, Research, and Weapons grades

## Slide 26: Critical Masses of Uranium & Plutonium as a Function of Isotopic Mix

## Slide 27: The weapons potential of high-assay low-enriched uranium

## Slide 28: Electric magnetic isotope separation (emis) exploits different weights of u235 and u238

## Slide 29: The Y-12 Plant at Oak Ridge, Tennessee used emis
The Y-12 Plant
Alpha Track Calutron at the Y-12 Plant at Oak Ridge, Tennessee

## Slide 30: EMIS “Calutron” was Discovered in Iraq in 1991

## Slide 31: Gaseous Diffusion also exploits different weights of u238 & u235

## Slide 32: 1st Gaseous Diffusion Plant was one of the world’s largest construction projects
K-25 Plant, Oak Ridge, Tennessee, The first gaseous diffusion plant

## Slide 33: French Gaseous Diffusion Plant is powered by 4 nuclear reactors
French gaseous diffusion plant powered by nearly 4 gigawatts electrical, four nuclear power reactors.

## Slide 34: Gas centrifuge Components

## Slide 35: The AVLIS (atomic vapor laser isotope separation) process

## Slide 36: Separation of Isotopes by Laser Excitation (SILEX): smaller, cheaper still

## Slide 37: Price and Proliferation Risk Comparison of Diffusion, Centrifuge, and SILEX Enrichment

## Slide 38: Basic stages of once-through uranium-based fuel cycles
Uranium Mining and Milling
Conversion to Uranium Hexafluoride (UF6)
Uranium Enrichment
Fuel Fabrication
Generating Nuclear Electricity
Spent Fuel Storage

## Slide 39: Fuel fabrication
Ceramic Uranium
Dioxide Pellets
Zirconium Alloy (or Similar)
Tubes for Cladding
Left: Individual fuel pellets.
Center: Pellets are assembled into a fuel rod
Right: Fuel rods are bundled together in a fuel assembly

## Slide 40: Fuel rod and fuel assembly process
A technician arranges fuel pellets in a trough before sliding the cladding over them.
Completed Fuel Rods
Fuel Rod Assembly
Fuel Assemblies in Reactor Core

## Slide 41: 3. What are the different types of nuclear reactors and how proliferation prone is each?

## Slide 42: Simplified Schematic of a Nuclear Reactor

## Slide 43: biggest Nuclear power plant components
Steam Turbines
Nuclear core and steam generators (during refueling)
Cooling Towers

## Slide 44: Major TYPES OF NUCLEAR REACTORs
Early Graphite Reactors
Magnox Reactor
Heavy Water Reactor (HWR)
Liquid-Metal Fast Breeder Reactor (LMFBR)
Light Water Reactors (LWR)—Pressurized (PWR) and Boiling (BWR)
RBMK
High-temperature Gas Cooled Reactor (HTGR)

## Slide 45: Reactor Species or groups

## Slide 46: First reactors: Graphite moderated
Chicago Pile-1
B Reactor

## Slide 47: Magnox Reactor: UK dual-use graphite design
Fuel | Natural Uranium
Moderator | Graphite
Coolant | Air
Refueling | On-load

## Slide 48: Wylfa MAGNOX Nuclear Plant, UK

## Slide 49: Yongbyon reactor: a magnox design

## Slide 50: Atomic Structure of heavy water D2O vs H2O
Frozen D2O (at right) sinks in light
water while frozen H2O floats

## Slide 51: Heavy Water Production
The Arak heavy water project located 120 miles southwest of Tehran
Whiteshell, UK

## Slide 52: Heavy Water Reactors
1. Fuel bundle
2. Calandria (reactor core)
3. Adjustor rods
4. Heavy water pressure reservoir
5. Steam generator
6. Light water pump
7. Heavy water pump
8. Fueling machines
9. Heavy water moderator
10. Pressure tube
11. Steam going to steam turbine
12. Cold water returning from turbine
13. Containment building of reinforced concrete

## Slide 53: Heavy Water Reactors Continued
Fuel | Natural uranium clad in zircaloy
Moderator | Heavy Water
Coolant | Heavy Water
Refueling | On-load

## Slide 54: On-Line Refueling—HWRs
CANDU Reactor

## Slide 55: Countries who operate or used to operate HWRs
Countries that operate HWRs: India, Argentina, Pakistan, Romania, Israel, China, and South Korea, Iran, Canada
Countries that used to operate HWRs: Germany, Sweden, Taiwan, and the United States, Russia, France

## Slide 56: IR-40 Heavy Water Reactor Near Arak, Iran

## Slide 57: Some Heavy water transmutes into tritium in hwrs. This tritium must be extracted for safety reasons but can also be used for h-bombs
Wosong Tritium Removal Facility: ROK Has Produced and Stockpiled Enough Tritium (4 kgs.) to Boost 1,000 Weapons

## Slide 58
Plutonium
Neptunium
Fast Neutron Reactions
Thermal Neutron Reactions
Popular neutron moderators include light water, heavy water, and graphite
CONVENTIONAL REACTORS EXPLOIT THERMAL REACTIONS, FAST REACTORS EXPLOIT FAST ONES
Weapons-grade plutonium

## Slide 59: Liquid Metal Fast Breeder Reactor (LMFBR): first reactor to produce electricity
Sodium-Cooled Fast Reactor
Fuel | Pu or MOX- clad in stainless steel
Moderator | None
Coolant | Liquid sodium
Refueling | Off-load

## Slide 60: Liquid Metal Fast Breeder Reactors also have been used to make bomb plutonium
India’s prototype fast breeder reactor under construction at Kalpakkam
Phénix, prototype fast breeder reactor in Marcoule, France – shut down in 2009

## Slide 61: fast breeder reactors are off-line fueled

## Slide 62: Fast Breeder reactor states
Countries that operate FBRs: China, Russia
Countries constructing FBRs: India, China
Countries with plans for FBRs, but not currently operating: Japan, South Korea, France, U.S.
Countries that have had FBRs in the past, but aren’t currently operating: U.S., France, U.K., Germany, Japan

## Slide 63
Superphenix, France, used to make bombs
Monju, Japan
Kalkar, Germany
Dounrey, UK
Enrico Fermi, Detroit
COMMERCIAL FAST BREEDERS: FAILED & ABANDONED

## Slide 64
Fast breeder reactor, India. To be used to make weapons
Fast breeder reactor, Russia. Over budget, completion delayed, tech exported to PRC
First 600 MWe fast breeder reactor, China
Experimental 20 MWe fast breeder reactor, China
Second 600 MWe fast breeder reactor, China
REMAINING BREEDERS: QUESTIONABLE

## Slide 65: Light-Water Reactor (PWR)
Typical Pressurized Water Reactor
Fuel | LEU
Moderator | Light Water
Coolant | Light Water
Refueling | Off-load

## Slide 66: First Light water reactor was designed for submarines

## Slide 67: Three Mile Island Nuclear Power Plant, U.S.

## Slide 68: Light-Water Reactor (BWR)
Typical Boiling-Water Reactor
Fuel | LEU
Moderator | Light Water
Coolant | Light Water
Refueling | Off-load

## Slide 69: Fukushima Daiichi Nuclear Power Plant, Japan

## Slide 70: LWRs are off-load fueled
LWR refueling

## Slide 71: RBMK (Reactor Bolshoy Moshchnosty Kanalny)
Fuel | LEU clad in zircaloy
Moderator | Graphite
Coolant | Light Water
Refueling | On-line

## Slide 72: Chernobyl Nuclear Power Plant, Ukraine

## Slide 73: High Temperature Gas Cooled Reactor
Fuel | Uranium clad in a graphite matrix
Moderator | Graphite
Coolant | Helium
Refueling | Off-load

## Slide 74: Fort St. Vrain Power Station was a one-off
Fort St. Vrain Power Station, HTGR. It operated from 1976 to 1989.

## Slide 75: On-Line Refueling—HTGC (pebble bed)
Under construction in China

## Slide 76: Generation iv Reactors

## Slide 77: Small Modular LWRs

## Slide 78: Fast Small Modular Reactor

## Slide 79: NuScale Reactor

## Slide 80: Summary of reactor characteristics by type
Type of Reactor | Magnox Reactor | High Temperature Gas- Cooled Reactor (HTGR) | Pressurized Water Reactor (PWR) | Boiling Water Reactor (BWR) | Heavy Water Reactor (CANDU) | Liquid Metal Fast Breeder Reactor (LMFBR)
Name of Example | Chapelcross (UK) | Fort St. Vrain (USA) | Zion (USA) | Browne Ferry 2 (USA) | Pickering (Canada) | Phenix (France)
Heat Output | 840 MWt | 842 MWt | 3250 MWt | 3293 MWt | 1744 MWt | 563 MWt
Electrical Output | 275 MWe | 330 MWe | 1050 MWe | 1065 MWe | 308 MWe | 233 MWe
Fuel | Natural Uranium Metal clad in Magnox alloy | Uranium carbide particles, enriched, coated in graphite matrix | Uranium oxide, 3% enriched, clad in Zirconium | Uranium oxide, 2.2% enriched, clad in zircaloy | Natural uranium oxide clad in zircaloy | Mixed uranium and plutonium oxide (MOX), 20 -27% enrichment, clad in stainless steel
Moderator | Graphite | Graphite | Light water | Light water | Heavy Water | None
Coolant | Carbon dioxide gas | Helium | Light water | Light water | Heavy water | Liquid sodium
Refueling | On-load | Off-load | Off-load | Off-load | On-load | Off-load

## Slide 81: Plutonium production by reactor type
Fissile Material Produced by a 1,000 MWe Reactor Operating at 70% Load Factor for One Year |  | 
Reactor Type | Initial Fuel (Enrichment) | Produced Pu (kg)
Light-Water Reactor | U235 (3%) | 175*
High Temperature Gas-Cooled Reactor | U235 (93%) | 29 (plus 64kg U235)
Canadian Deuterium-Uranium (CANDU) | U (natural) | 360
Fast Breeder Reactor | MOX | 300
* For a LWR that has been operating for over 36 months. Note that low-enriched reactors produce more plutonium than high enriched reactors (the fast breeder reactor uses plutonium as fuel, so much of what is produced will actually be reused as fuel). Again, production in a CANDU is the highest for a given power generation. |  | 

## Slide 82: 4. What can be done with spent reactor nuclear fuel?

## Slide 83: Direct Disposal vs. Reprocessing

## Slide 84: Commercial Reprocessing: a major undertaking
Rokkasho, Japan: over 20 billion spent, under construction since 1993

## Slide 85
E. ASIA REPROCESSING: A FUTURE HEADACHE
PRC 50 tHM/yr Pilot plant: ~100 bombs worth of plutonium/yr
Possible PRC 800 tHM/yr EDF plant: ~1200+ bombs worth of pu/yr
Japan’s 800 tHM/yr plant: ~1,200+ bombs’ worth pu/yr, to open 2023
ROK Experimental Pyroprocessing Facility, funding frozen
1st PRC 200 tHM/yr plant under construction to be on line by 2025
2nd PRC 200 tHM/yr reprocessing plant to be on line before 2030

## Slide 86: Ferguson Culler Design: Small, cheap, and quick

## Slide 87: Reprocessing steps
Cooling
Head-end treatment
Separation/Extraction
Conversion of plutonium nitrate to plutonium oxide
Storage of radioactive wastes

## Slide 88: cooling
Cooling Pool

## Slide 89: Head-end treatment
Head-End Process

## Slide 90: Separation/extraction
PUREX – Extraction Process
Windscale reprocessing towers

## Slide 91: Reprocessing Pulse Column

## Slide 92: Plutonium Uranium Extraction Plant at Hanford, Washington

## Slide 93: Cooling Pools for Spent Fuel

## Slide 94: Dry cask storage

## Slide 95: Additional Slides

## Slide 96: Critical Masses of Uranium & Plutonium as a Function of Isotopic Mix

## Slide 97: Estimated Yields for Different Bomb Technologies Using LWR Pu
Chart: Estimated yield in kilotons (kt)
| 1945 Tech | 1950 Tech | 1970 Tech
Weapons Grade, 6% 240 Pu content | 13 | 15 | 16
One-cycle LWR Pu, 14% Pu 240 content | 5 | 10 | 12

## Slide 98: IAEA Safeguards guidelines
Direct Use Materials | Significant Quantity
Pu | 8 kg total element (containing less than 80% Pu-238)
U-233 | 8 kg total isotope
HEU | 25 kg contained U-235
Indirect Use Materials | Significant Quantity
LEU (U-235 <20%) | 75 kg contained U-235 (include natural and depleted U)
Thorium | 20 tons total element
Material | Timeliness Goal
Non-irradiated direct use (Pu in fresh fuel) | One Month
Irradiated direct use (e.g. Pu in spent fuel) | Three Months
Indirect use (e.g. LEU) | One Year

## Slide 99: Basic IAEA Safeguards Methods
Example of IAEA Containment
Example of IAEA Surveillance

## Slide 100: Schematic of Fukushima accident

## Slide 101: Pyroprocessing
“South Korea also has advanced reprocessing technology. One professor of nuclear engineering said that "our capabilities when it comes to pyroprocessing, which involves reprocessing by using electolysis, are world-class.”
Chosun Ilbo, February 19, 2016
Planned ROK Pyroprocessing Plant

## Slide 102: Wolsong Heavy Water Reactors
From the four CANDU-6 reactor cores and spent fuel at Wolsong, the RoK could recover 150 kg of lower-burnup fuel-grade plutonium (discharged during the first cycle after start-up—100 to 400 full-power days after start-up) and about 220 kg of higher burnup fuel-grade plutonium that could be used to fabricate more than 50 nuclear warheads with yields exceeding 20 kilotons based on pure fission solid core, levitated core or hollow core designs.

## Slide 103: ROK Has Produced and Stockpiled Enough Tritium (4 kgs.) to Boost 1,000 Weapons
Wosong Tritium Removal Facility

## Slide 104: Too Much Planned Japanese Plutonium for Any Peaceful Purpose
Rokkasho now may open Fall 2022

## Slide 105: Enriching Uranium For What?
Rokkasho Uranium Enrichment Plant
Japan by 2022 could produce up to ~6,400 kg HEU/year or more than 500 bombs worth per year

## Slide 106: Japan Can Master Boosting and More
The National Institute for Fusion Science (NIFS) in Toki
Japan Atomic Energy Agency’s (JAEA) Naka Fusion Institute, Ibaraki Prefecture
As its contribution to the International Thermonuclear Experimental Reactor (ITER) under construction in France, Japan will provide much of the high-tech components and will host an €1 billion materials testing facility – the International Fusion Materials Irradiation Facility (IFMIF).
Naka Fusion Institute, which includes the Tritium Processing Laboratory
National Institute of Fusion Research

## Slide 107: Estimated Warhead Inventories: PRC, US, Russia
Chart: # of Nuclear Warheads
| China | United States | Russia
Strategic (Deployed) | 1590 | 1950
Tactical (Deployed) | 150
Tactical (Storage) | 2000
Reserve | 250 | 2740 | 720
Awaiting Dismantlement | 2340 | 2700
Source: http://www.tandfonline.com/doi/full/10.1080/00963402.2016.1264213 and http://www.tandfonline.com/doi/full/10.1080/00963402.2017.1290375

## Slide 108: What if China Develops Many MIRVs?
According to the Belfer Center’s Hui Zhang, China’s limited fissile material stockpile means that the country does not have the ability to build significantly more warheads without restarting fissile material production.”
BAS March 24, 2015, Tong and Logan

## Slide 109: What About Chinese Tactical Nuclear Weapons?
China developed and tested a neutron bomb in 1988 as a “technological reserve” - Liu Huaqiu, Senior Chinese Nuclear Scientist
Will China need tactical nuclear weapons to counter the U.S., its allies, or Russia?

## Slide 110: Stocks of Highly Enriched Uranium
Chart: Metric Tons of Highly Enriched Uranium
| China | United States | Russia
Military | 16 | 260 | 616
Naval (fresh) | 152 | 20
Naval (spent | 100 | 10
Civilian | 20 | 20
Excess (mostly for blendown) | 63 | 29
(18 tons)
± 4 uncertainty
(599 tons)
(679 tons)
Source: http://fissilematerials.org/library/gfmr13.pdf and http://fissilematerials.org/library/gfmr10.pdf

## Slide 111: Projected PRC Enrichment Surpluses Beyond Power Requirements ~ 1,500 Bombs a Year
China’s has an estimated surplus of ~19,000 kg HEU
232 SWU required to make 1 kg HEU
Conservatively, in 2020, over 2,500 weapons worth for PRC, over 300 for Japan
120,000 SWU required to refuel 1-GWe reactor with LEU annually (66 GWe PRC, 12.5 GWe Japan in 2020)
Hanzhong and Lanzhow

## Slide 112: Projected Uranium Enrichment Surpluses in East Asia
Projected enrichment
supply vs demand until 2035

## Slide 113: Tons of Separated Plutonium
Chart: Metric Tons Separated Plutonium
| China | United States | Russia
Military | 1.8 | 38.3 | 88
Excess military material | 49.3 | 34
Additional strategic stockpile | 6
Civilian stockpile | 49.5
(1.8 tons assumed)
(87.6 tons)
(169.5-185.5 tons)
± 8 tons uncertainty
Source: http://fissilematerials.org/library/gfmr13.pdf and http://fissilematerials.org/library/gfmr10.pdf

## Slide 114: PRC’s Limited Plutonium Production Capacity Is the Bottleneck to Many More Weapons
PRC has only 2 plutonium production reactors
One is being dismantled
One hasn’t operated since the early 1990s
If restarted, the single reactor could produce roughly 300kg of plutonium a year, only enough to make roughly 75 plutonium triggers or bombs.
Jiuquan plutonium production reactor

## Slide 115: PRC’s Most Immediate Alternative Plutonium Production Option: Its Heavy Water Reactors
Two Candu-6 reactors (600 MWe each) at Qinshan
Capable of producing ~650 kilograms of plutonium a year
Sufficient for roughly >100 bombs a year
Source: https://en.wikipedia.org/wiki/CANDU_reactor

## Slide 116: 1987: Reagan Administration Proposed Using WPSS LWR to Make Weapons Plutonium
Source: http://www.historylink.org/index.cfm?DisplayPage=output.cfm&File_Id=5482

## Slide 117
4 kg weapons-grade Pu assumed per bomb based on DOE estimate.
5.2 kg reactor-grade Pu assumed per bomb based on estimate by Richard L. Garwin (see http://fas.org/rlg/980826-pu.htm)
150 kg weapons-grade Pu conservatively assumed per reactor year (see page 64, http://fsi.stanford.edu/sites/default/files/VAF-June.pdf)
250 kg reactor-grade Pu conservatively assumed per reactor year.
HOW MUCH PLUTONIUM COULD A 1 GWE LWR GENERATE/YEAR?
250 kg
10,000 kg
Chart: Pu (kg) produced per year
| 1 AP1000 reactor
Weapons-grade Pu | 150
Reactor-grade Pu | 250

## Slide 118: PRC’s Other Plutonium Production Bottleneck: Lack of a Large, Reliable Reprocessing Plant
China has decommissioned its large military reprocessing plant

## Slide 119: Solution 1: Buy French Reprocessing plant
Presidents Francois Hollande and Xi Jinping
France agrees to build PRC a large commercial reprocessing plant at Jianyuguan
Planned 800 tHM/yr EDF plant: ~1600 bombs worth of pu/yr

## Slide 120: Solution 2: build and operate your own reprocessing plants
China 200 tHM/year reprocessing plant under construction, operational by 2025? 2,000 kgs pu/yr
Images of 50tHM/year Chinese Reprocessing plant at the Jiuquan Atomic Energy Complex, fully operational 2017, 500 kgs pu/yr

## Slide 121
CHINESE FAST REACTORS
China Experimental Fast Reactor, 20 MWe, operational 2010
China Fast Reactor, 600 Mwe (110 wfpu/year), operational 2026?

## Slide 122
EAST ASIAN REPROCESSING PLANTS
50 tHM/yr Pilot plant: ~100 bombs worth of plutonium/yr
Planned 800 tHM/yr EDF plant: ~1600 bombs worth of pu/yr
200 tHM/year plant is now under construction: ~400 bombs worth of pu/yr
800 tHM/yr Rokkasho plant: ~1,600 bombs’ worth pu/yr, 2021 planned opening
ROK Experimental Pyroprocessing Facility