## Slide 1: Nuclear and non-nuclear energy trends
A presentation by Henry Sokolski Executive Director Nonproliferation Policy Education Center www.npolicy.org
© Nonproliferation Policy Education Center

## Slide 2: Questions to be Answered
Why bother with energy economics?
What are the basics of electricity production, consumption, distribution, and storage that help determine the costs of different electrical options?
How do nuclear and non-nuclear forms of energy perform economically at home and abroad?

## Slide 3: Short answer to Question I
A. Assessing the quality of a country’s energy policies is a way to assess how sound its government is.
B. If an energy activity is uneconomic (e.g. reprocessing nuclear fuel), countries ought to be less insistent they have an inalienable right to pursue it. In this way, energy market signals might fortify nuclear nonproliferation (or not).
C. Assessing the costs of electrical power, distribution, and storage systems helps discern likely energy futures.

## Slide 4: Short Answer to Question II
They’re complicated

## Slide 5: short Answer to Question III
Natural gas is still replacing coal much more than nuclear power is both here and abroad.
Renewables and electrical storage will compete against future investments in natural gas over the next two decades
Nuclear power’s economic future depends on: 1) making a design breakthrough that makes it far less costly and 2) how willing nations are to subsidize nuclear energy to overrule market signals
Distribution and storage innovations could reduce demand for any type of large electrical generator
Demand to reduce greenhouse gases, even if it’s taxed, is unlikely to change the above

## Slide 6: II. Electric power basics

## Slide 7: Basic electrical grid

## Slide 8: Alternating and direct current
AC Transformer basics

## Slide 9: DC voltage lines Will become more prevalent in advanced economies

## Slide 10: Base and peak load power demand

## Slide 11: Popular Base load electrical generators
COAL
NATURAL GAS
HYDRO
NUCLEAR

## Slide 12: Popular Peak load generators Small natural gas, diesel, propane-fueled plants

## Slide 13: electrical distribution systems

## Slide 14: N. American transmission system is Mature, complex, and international

## Slide 15: European electrical grids are also robust
http://ses.jrc.ec.europa.eu/gas-and-power-modelling

## Slide 16: L. America, Africa, Middle East electrical transmission lags behind

## Slide 17: E. Asia's current national grids are suboptimal

## Slide 18: Microgrids: an Alternative to centralized generation

## Slide 19: Islanding allows connection to the grid and the ability to work independently of it

## Slide 20: III. Economics of Nuclear vs. non-nuclear power: natural gas substitution for coal and nuclear

## Slide 21: US natural gas: firing more electrical generation
https://www.eia.gov/todayinenergy/detail.php?id=42655
https://www.eia.gov/todayinenergy/detail.php?id=55960#:~:text=We%20forecast%20that%20the%20solar,year%20to%2017%25%20in%202023.

## Slide 22: US natural gas resources, 2016
https://www.eia.gov/maps/maps.htm

## Slide 23: Henry Hub natural gas spot price
Current Spot Price: 2.34 (October 2024)
https://www.eia.gov/dnav/ng/hist/rngwhhdd.htm

## Slide 24: Spot price of European natural gas
https://ycharts.com/indicators/europe_natural_gas_price

## Slide 25: Global shale gas basins, top reserve holders
https://www.researchgate.net/figure/Global-Shale-Gas-Basins-Source-EIA-Reuters-Refs-14-19-Advanced-Resources-Inc_fig1_323691748
February 2018

## Slide 26: Levantine and Zohr: Massive natGAS discoveries

## Slide 27: Recent UAE gulf and Turkish Black sea gas discoveries
https://www.spglobal.com/platts/es/market-insights/latest-news/natural-gas/020320-adnoc-to-develop-huge-onshore-gas-find-near-dubai
https://www.google.com/imgres?imgurl=https://steelguru.com/uploads/news/turkey-black-sea-natural-gas-discovery_5704.jpg&imgrefurl=https://steelguru.com/gas-oil/turkey-announces-black-sea-natural-gas-discovery/562466&tbnid=aP0BTkaLcb9fhM&vet=1&docid=fY4K_2qraRB1yM&w=1668&h=1000&hl=en&source=sh/x/im
The biggest gas find in 15 years, UAE now self sufficient

## Slide 28: Saudi Arabia New Gas Options
https://interfaxenergy.com/article/22179/saudi-aramco-presses-on-with-shale-gas
https://www.eia.gov/beta/international/analysis_includes/countries_long/Iran/pdf/iran_bkgd.pdf
2 reactors at $12-24 b versus $334 billion for shale gas development by 2025

## Slide 29: Iranian Gas
https://www.wsj.com/articles/iran-seeks-rapid-reboot-for-natural-gas-exports-1453821547
https://www.eia.gov/beta/international/analysis_includes/countries_long/Iran/pdf/iran_bkgd.pdf
Notes: Stop here for end of part 1

## Slide 30: Economics of Nuclear vs. non-nuclear power

## Slide 31: Abating carbon should start with the cheapest, quickest methods 1st
Source: Exelon
Million Metric Tons of CO2 per Year
Coal Retirements
Energy Efficiency
Nuclear Uprates
Coal-to-Gas Switch
Solar Photovoltaic
New Natural Gas Plant
Wind Power
New Nuclear Plant
Clean Coal with CCS
White line represents price after including effects of tax incentives or loan guarantees
Million Metric Tons of CO2 per Year
Dollars per Metric Ton of CO2 (in 2016$)
Solar PV: $675 / $300 with incentives
Clean Coal: $600 / $350 with incentives
200
150
100
50
0
(50)
40 60 80 100 120 140 160

## Slide 32: Break Even #s for building New nuclear Makes government subsidies essential
To build a reactor in 2011 cost $9.8 billion. In 2024 dollars, that reactor would cost $18.44 billion to build – 88% more. This increases the natural gas break even price to $20.64 per MBTU and the CO2 tax number to $46.90 per ton.
Spot natural gas prices: CO2 Gas Number:
US: $2.34 MBTU No national market
EU: $11.78 MBTU $68.16 per ton
East Asia: $15.65 MBTU No market
Bottom Line: Nuclear construction today only makes sense where government weighs in heavily – Europe and China.

## Slide 33: So far, Overnight reactor costs have only climbed
Overnight cost in 2017 £6,666 per kilowatt Vogtle 3 and 4 ($10,000)

## Slide 34: levelized costs are rising as well

## Slide 35
TODAY, LARGE REACTOR BUILDS CAN’T COMPETE ECONOMICALLY WITH NONNUCLEAR ALTERNATIVES - 2024

## Slide 36: This Has Discouraged New Large Reactor Builds

## Slide 37: The Economic Case for Small Reactors, Advanced and Modular
Cost less (individually projected to cost $1 - $3 billion, not $14 billion)
Should fit more readily on the grid and can be sited nearer customers to afford district or commercial heating
Many may not need to be refueled frequently
Don’t emit carbon

## Slide 38: With Bigger reactors, Capital Costs of Producing Electricity Should Decline. with small reactors, electricity prices decline if reactors are cheap

## Slide 39: The economic case against small and advanced modular reactors
Small reactors may have difficulty achieving scale of economies (promoters presume mass production will overcome high capital cost/installed KW). History suggests otherwise.
Most proposed small reactors rely on new fuels that require significant government development and support
Most “advanced” small reactors toy with historically costly fast reactor technologies—use plutonium or HEU or at least 20%
There are cheaper, quicker ways to reduce greenhouse gases
Some of the proposed designs are not so small

## Slide 40: Yet, Historically “Advanced” Fast Reactors Have Proved the Most Costly to Build

## Slide 41: Nonnuclear Economic Competition Is Projected to Get Stiffer
2021 there were 56 gigawatt hours of grid battery storage deployed worldwide
https://about.bnef.com/blog/global-energy-storage-market-to-grow-15-fold-by-2030/
https://en.wikipedia.org/wiki/Levelized_cost_of_electricity

## Slide 42: Grid battery storage is coming down as well
https://atb.nrel.gov/electricity/2022/utility-scale_battery_storage

## Slide 43: New energy technology developments reinforce move away from nuclear and coal

## Slide 44: Smart grids balance a wide # of electrical sources & reduce base load requirements

## Slide 45: Technologies for smart grids Super Capacitors, Switches, Batteries, Direct Current Systems
MICRO
SUPERCAPACITOR
WIND FARM
BATTERY BANK
SMART
MONITOR
High Voltage Direct Current Grid

## Slide 46: Technologies for Smart grids also can be used in distributed systems

## Slide 47: Distributed electrical systems would make the grid a backup system

## Slide 48: The grid Management challenge renewables present

## Slide 49: Lithium discoveries in the united States

## Slide 50: Lithium-Ion Giga-battery factories
Netherlands
planned Brandenburg
https://merics.org/en/analysis/chinas-battery-industry-powering-global-competition
Nevada

## Slide 51: Other kinds of batteries
Flow battery, California, 2 megawatt 8 megawatt hours
Utah plans 1 gigawatt

## Slide 52: More Batteries
Concentrated solar plant, Spain
Pumped storage

## Slide 53: Battery storage is increasing natural gas’s competitive edge

## Slide 54: Renewables are becoming more attractive in the middle east

## Slide 55: The middle east is rich in renewable energy potential

## Slide 56: Concentrated Solar Power Costs: Now Well Below Nuclear

## Slide 57: Saudi Arabia’s Best Bet is Not Nuclear
Source: Qamar research
Chart: Electricity price (c/kWh)
| GAS CCGT, $12/MMBTU | DIESEL TURBINE, $50/BBL | NUCLEAR | ONSHORE WIND | GAS CCGT, $6/MMBTU | SOLAR CSP | SOLAR ROOFTOP | COAL CCS | GAS CCS, $6/MMBTU | CONVENTIONAL COAL | GAS CCGT, $1/MMBTU | SOLAR PV
TRANSMISSION & DISTRIBUTION | 1.03 | 1.03 | 3.24 | 1.03 | 1.03 | 1.03 | 1.03 | 1.03 | 1.03 | 1.03 | 1.03
LOW CASE | 13.4 | 10.66 | 7.12 | 9 | 8 | 7.3 | 6.92 | 5.51 | 5.27 | 4.07 | 3.5 | 2.99

## Slide 58: Uranium: Plentiful and Cheap ~$65.29/pound, 08/2024
https://world-nuclear.org/information-library/nuclear-fuel-cycle/uranium-resources/uranium-markets.aspx
https://ycharts.com/indicators/uranium_spot_price#:~:text=Uranium%20Spot%20Price%20is%20at,9.16%25%20from%20one%20year%20ago.

## Slide 59: Enrichment Services: Climbing on speculation ($106.97/SWU 10/24 Spot)
https://seekingalpha.com/article/4556160-centrus-energy-reiterating-bullish-thesis

## Slide 60: Future Non-Economic variables of interest

## Slide 61: Energy Intensity of GDP is declining

## Slide 62: Current global warming models assume median population growth

## Slide 63: It’s unclear if population will decline or rise after 2040

## Slide 64: Fertility has declined with Education
https://ourworldindata.org/grapher/womens-educational-attainment-vs-fertility

## Slide 65: We still waste more than half the energy we produce

## Slide 66: If you were to invest in electricity production, and wanted a positive return on your investment in less than 5 years, which would you pick? - Nuclear - gas - renewables - interconnection and switching technology - battery storage

## Slide 67: Additional Slides

## Slide 70: Theoretically, As Reactors Get Bigger, the Capital Costs of Producing Electricity Should Decline
The larger the reactor, the more electricity it produces. Making them bigger was supposed to reduce the cost of an installed kilowatt hour

## Slide 71
Today, Large Reactor Builds Can’t Compete Economically with Nonnuclear Alternatives

## Slide 72: This Has Discouraged New Reactor Builds

## Slide 73: As Reactors Grew Larger, Economics Recommended that Containment Requirements Be Loosened Fuel Failures and Core Meltdowns Were Presumed Unlikely
Three Mile Island, 2x 812 MWe
Hallam Nuclear Power Plant, 240 MWe, 1962

## Slide 74: And Even with More Lax Containment Requirements, Reactor Complexity, Construction Costs Still Grew

## Slide 75: Increased Costs Have Hardly Encouraged Nuclear Industry to Cover Full Liabilities, which, in Turn, Discourages Industry from Making Safety Investments
Fukushima: $200 b to >$700 b.
Chernobyl: >$200 b
Three Mile Island ~$1.78 b

## Slide 76: The Safety Case for Small Reactors, Advanced and Modular
Small reactors produce less radiation and waste per reactor
Some designs can be passively cooled (without pumps), “self-regulating”
Can incorporate most nuclear components within a single pressurized vessel
Can be built underground

## Slide 77: Unkind History: Previous Small Reactors Proved Too Small to Compete Economically
Fermi 1, 69 MWe
Elk River, 22 MWe
LaCrosse, 50 MWe
Fort St. Vrain, 185 MWe
Punta Higuera, Puerto Rico, 17 MWe
Piqua, Ohio, 12 MWe

## Slide 78
SLIMM
Energy Multiplier Module
PRISM reactor
Toshiba 4s Reactor
DOE Now Wants Small Reactors to Go Fast
Molten Chloride Fast Reactor
Traveling Wave Reactor

## Slide 79: Yet, Historically Fast Reactors Have Proved the Most Costly to Build

## Slide 80: To Help Out, DOE Plans to Spend Billions on Advanced Nuclear Fuels in Support of SMRs
Versatile Test Reactor, $3-6 B
American Centrifuge Plant, Pinkerton, OH or DOE alternative, $10 B?

## Slide 81: The Economic Competition Is Projected to Get Stiffer
2018 there were 12 gigawatt hours of grid battery storage deployed worldwide

## Slide 82: Industry Counting on Exporting Small Reactors to the Middle East
SMART Reactor, Saudi Arabia
NuScale Reactor, Jordan
Jordan

## Slide 83: What nuclear activities make money
Existing Uranium enrichment
Nuclear fuel fabrication ~ $23 billion
Production of industrial, agricultural, and medical isotopes ~ $30 billion

## Slide 84: Safety is a much bigger issue
Global City Populations
Low & High Nuclear Growth Scenarios

## Slide 85: Sound nuclear safety methodology: What's currently lacking internationally
NRC argues
Risk = Probability x Consequence
(focuses on prompt deaths, exposure calculations, assumes evacuation success, manipulates calculations for "reactor years" between accidents).
Concludes probability is too low to question safety
Nuclear industry refuses to assume any risk whatsoever for off-site damage in the case of nuclear accidents

## Slide 86: Uncertain energy futures: last half of the 19th century
Lighting: Whale oil, gas, candle, electricity
Heating: Oil, coal, gas, wood, electricity
Locomotion: Steam, electricity, gasoline, diesel
Electricity: AC, DC

## Slide 87: Uncertain energy futures: 1950
Lighting: Electricity (centrally generated, grid distributed)
Heating: Gas, electric, fuel oil
Locomotion: Gasoline, diesel
Electricity: AC, Coal, oil fueled, hydro

## Slide 88: Uncertain energy futures: Next Half century
Lighting: Incandescent, fluorescent, LED
Heating: Electricity, gas, biomass, solar, geothermal
Locomotion: Electric vehicles, gasoline, fuel cell, diesel
Electricity: AC, DC, distributed, central, flow batteries, fuel cells, smart switching, photovoltaics, small reactors

## Slide 89: Electrical grid resilience basics

## Slide 90: Distribution of energy interruptions

## Slide 91: US energy interruptions: 2012-2016

## Slide 92: Causes of energy interruptions
Trees/Weather
Vegetation
Ice Storms
Equipment Failure

## Slide 93: Squirrels, other animals are also a problem
Confirmed power outages caused by Squirrels in 2017
Power outages caused by animals since 1987
Source: https://cybersquirrel1.com/

## Slide 94: What can be done to reduce outages?
Go off-grid
Upgrade local electrical repair teams
Clear trees and vegetation
Create a transformer reserve for quick replacement

## Slide 95: What interruptions government officials focus on is a function of their authority

## Slide 96: Gas distribution is growing but still disconnected

## Slide 97: Levelized Energy cost Comparisons after Fukushima
Source: Lazard “Levelized Cost of Energy Analysis - Version 10.0”

## Slide 99: An Alternative: An electric connected asia

## Slide 100: US Carbon abatement: coal retirements and gas substitutes
https://www.eia.gov/todayinenergy/detail.php?id=7290 and
https://www.eia.gov/todayinenergy/images/2016.05.19/main.png

## Slide 101: US carbon emissions flat to declining
https://www.mprnews.org/amp/story/2020/04/08/us-greenhouse-gas-emissions-may-fall-75percent-in-2020

## Slide 102: “Beijing to shut all major coal power plants to cut pollution”–Bloomberg News, March 23, 2015
China aims to shut 8.7 GW of coal power by year-end – regulator – Reuters, September 29, 2019 (1,000 GWe of coal power still operating today)

## Slide 103: After Covid, Beijing is burning lots of coal
https://www.statista.com/statistics/265491/chinese-coal-consumption-in-oil-equivalent/
https://en.wikipedia.org/wiki/Coal_in_China

## Slide 104: China projected to build 270 GW of new coal – burning generators by 2025

## Slide 105: Profitability outlook for all us nuclear plants, 2017-2019

## Slide 106: US Large Reactor growth likely to be negative
https://www.nytimes.com/interactive/2018/06/13/climate/coal-nuclear-bailout.html

## Slide 107: Nuclear retirements until recently, were Clearly outstripping construction in Europe

## Slide 108: This was also happening in Japan and South Korea
Chart: 
2022 | 24
2034 | 17
Number of Nuclear Reactors in South Korea, Current and Projected https://en.yna.co.kr/view/AEN20220310003900320#:~:text=South%20Korea%20now%20has%20a,total%20power%20generation%20by%202030
In 2021, ROK nuclear = 27.4%
New plan for 2030 ~ 30%
Japan ~ 20% by 2030

## Slide 109: Nuclear growth in China, slowing down
Chart: 
| 2021 | 2025 | 2030
Offical Projection (GW) | 55 | 70 | 150
Likely (GW) | 120
https://asia.nikkei.com/Business/Energy/China-greenlights-6-new-nuclear-reactors-in-shift-away-from-coal

## Slide 110: Allam Cycle Generator: Economic, Zero Emissions at 4-5 cents/KWh?

## Slide 111: Unkind History: earlier Small Reactors were Too Small and unreliable to compete
Fermi 1, 69 MWe
Elk River, 22 MWe
LaCrosse, 50 MWe
Fort St. Vrain, 185 MWe
Punta Higuera, Puerto Rico, 17 MWe
Piqua, Ohio, 12 MWe

## Slide 112: More Unkind History: Gen III Reactors Also Were Modular
Two ACP100 modular reactors have been given construction go ahead Brian Wang | November 17, 2011 (projected to come online 2013 but didn’t)

## Slide 113
SLIMM
Energy Multiplier Module
PRISM reactor
Toshiba 4s Reactor
DOE NOW WANTS SMALL REACTORS TO BE “ADVANCED”-- FAST
Molten Chloride Fast Reactor
Traveling Wave Reactor

## Slide 114: To Help Out, DOE Plans to Spend Billions on Advanced Nuclear Fuels in Support of SMRs
Versatile Test Reactor, $3-6 B
American Centrifuge Plant, Pinkerton, OH or DOE alternative, $10 B?