## Slide 1
NUCLEAR ENERGY BASICS,
PART 2:
REACTORS AND NUCLEAR FUEL MAKING
A presentation by Henry Sokolski Executive Director Nonproliferation Policy Education Center www.npolicy.org
© Nonproliferation Policy Education Center

## Slide 2: Question 1:
What are the basic stages of once-through uranium based fuel cycles?

## Slide 3: Answer 1:
There are six stages: Uranium mining and milling, conversion to uranium hexafluoride (UF6), uranium enrichment, fuel fabrication, generating nuclear electricity, spent fuel storage.

## Slide 4: Question 2:
What are the most popular methods of enriching uranium?

## Slide 5: Answer 2:
Centrifuges and gaseous diffusion

## Slide 6: Question 3:
What are the different types of nuclear reactors and how proliferation prone is each?

## Slide 7: Answer 3:
All types of reactors can make nuclear explosive plutonium– light water and heavy water reactors, gas cooled and graphite reactors, RMBK and fast reactors

## Slide 8: Question 4:
What can be done with spent reactor nuclear fuel?

## Slide 9: Answer 4:
Spent fuel can be recycled or not. In either case, there will be considerable waste that must be stored above or under ground.

## Slide 10: 0. Nuclear Fuel Cycle Basics

## Slide 11: There are two Major Paths to the Bomb

## Slide 12: U238 & U235: two important uranium isotopes
U238
Has 146 neutrons
constitutes 99.3% of uranium in nature
Is not prone to fission
U235
Has 143 neutrons
Constitutes .7% of uranium found in nature
Is prone to fission

## Slide 13: Uranium centrifuge enrichment separates the heavy uranium from the light uranium

## Slide 14: There are two Major Paths to the Bomb

## Slide 15: Uranium Transmutes to Plutonium in a Reactor

## Slide 16: Spent Reactor Fuel Contains Plutonium That Can Be Chemically Stripped Out (Reprocessed)

## Slide 17: 1. What are the basic stages of once-through uranium based fuel cycles?

## Slide 18: Once-Through Fuel Cycle doesn’t reprocess spent fuel
FIGURE 1

## Slide 19: Closed Plutonium-Based Fuel Cycle requires reprocessing
FIGURE 2

## Slide 20: Basic stages of once-through uranium-based fuel cycles

## Slide 21: Basic stages of once-through uranium-based fuel cycles
Uranium Mining and Milling
Conversion to Uranium Hexafluoride (UF6)
Uranium Enrichment
Fuel Fabrication
Generating Nuclear Electricity
Spent Fuel Storage

## Slide 22: Step 1: Uranium Mining
Major uranium producers 2016

## Slide 23: Conventional uranium Mining
Underground
Open Pit

## Slide 24: In Situ Recovery mining method
1. Injection Wells
2. Recovery Wells
3. Monitoring Wells

## Slide 25: yellowcake

## Slide 26: Basic stages of once-through uranium-based fuel cycles
Uranium Mining and Milling
Conversion to Uranium Hexafluoride (UF6)
Uranium Enrichment
Fuel Fabrication
Generating Nuclear Electricity
Spent Fuel Storage

## Slide 27: Step 2: Conversion to Uranium Hexafluoride
UF4 (Green Salt) and uf6 (Uranium hexafluoride)

## Slide 28: Hexafluoride Conversion Facility– large & rare
Port Hope in Ontario, Canada

## Slide 29: Major hexafluoride uf6 producers
[t U/year] metric tons uranium/year

## Slide 30: 2. What are the most popular methods of enriching uranium?

## Slide 31: Step 3: Uranium Enrichment
Most countries that enrich uranium use centrifuges.
Gaseous Diffusion: Argentina
Centrifuge: Brazil, U.S.-URENCO, Holland, France, UK, Germany, Russia, China, Japan, Iran, India, Pakistan, North Korea

## Slide 32: The effort needed to enrich U to 3-5% is half of what is needed to enrich to Weapons-Grade u
Separative Work Units Needed to Enrich Uranium to Power, Research, and Weapons grades

## Slide 33: Critical Masses of Uranium & Plutonium as a Function of Isotopic Mix

## Slide 34: The weapons potential of high-assay low-enriched uranium

## Slide 35: Electric magnetic isotope separation (emis) exploits different weights of u235 and u238

## Slide 36: The Y-12 Plant at Oak Ridge, Tennessee used emis
The Y-12 Plant
Alpha Track Calutron at the Y-12 Plant at Oak Ridge, Tennessee

## Slide 37: EMIS “Calutron” was Discovered in Iraq in 1991

## Slide 38: Gaseous Diffusion also exploits different weights of u238 & u235

## Slide 39: 1st Gaseous Diffusion Plant was one of the world’s largest construction projects
K-25 Plant, Oak Ridge, Tennessee, The first gaseous diffusion plant

## Slide 40: French Gaseous Diffusion Plant is powered by 4 nuclear reactors
French gaseous diffusion plant powered by nearly 4 gigawatts electrical, four nuclear power reactors.

## Slide 41: Gas centrifuge Components

## Slide 42: The AVLIS (atomic vapor laser isotope separation) process

## Slide 43: Separation of Isotopes by Laser Excitation (SILEX): smaller, cheaper still

## Slide 44: Price and Proliferation Risk Comparison of Diffusion, Centrifuge, and SILEX Enrichment

## Slide 45: Basic stages of once-through uranium-based fuel cycles
Uranium Mining and Milling
Conversion to Uranium Hexafluoride (UF6)
Uranium Enrichment
Fuel Fabrication
Generating Nuclear Electricity
Spent Fuel Storage

## Slide 46: Step 4: Fuel fabrication
Ceramic Uranium
Dioxide Pellets
Zirconium Alloy (or Similar)
Tubes for Cladding
Left: Individual fuel pellets
Center: Pellets are assembled into a fuel rod.
Right: Fuel rods are bundled together in a fuel assembly.

## Slide 47: Fuel rod and fuel assembly process
A technician arranges fuel pellets in a trough before sliding the cladding over them.
Completed Fuel Rods
Fuel Rod Assembly
Fuel Assemblies in Reactor Core

## Slide 48: 3. What are the different types of nuclear reactors and how proliferation prone is each?

## Slide 49: Step 5: Generating Nuclear Electricity
Simplified Schematic of a Nuclear Reactor​

## Slide 50: biggest Nuclear power plant components
Steam Turbines
Nuclear core and steam generators (during refueling)
Cooling Towers

## Slide 51: Major TYPES OF NUCLEAR REACTORs
Early Graphite Reactors
Magnox Reactor
Heavy Water Reactor (HWR)
Liquid-Metal Fast Breeder Reactor (LMFBR)
Light Water Reactors (LWR)—Pressurized (PWR) and Boiling (BWR)
RBMK
High-temperature Gas Cooled Reactor (HTGR)

## Slide 52: Reactor Species or groups

## Slide 53: First reactors: Graphite moderated
Chicago Pile-1
B Reactor

## Slide 54: Magnox Reactor: UK dual-use graphite design
Fuel | Natural Uranium
Moderator | Graphite
Coolant | Air
Refueling | On-load

## Slide 55: Wylfa MAGNOX Nuclear Plant, UK

## Slide 56: Yongbyon reactor: a magnox design

## Slide 57: Atomic Structure of heavy water D2O vs H2O
Frozen D2O (at right) sinks in light
water while frozen H2O floats

## Slide 58: Heavy Water Production
The Arak heavy water project located 120 miles southwest of Tehran
Whiteshell, UK

## Slide 59: Heavy Water Reactors
1. Fuel bundle
2. Calandria (reactor core)
3. Adjustor rods
4. Heavy water pressure reservoir
5. Steam generator
6. Light water pump
7. Heavy water pump
8. Fueling machines
9. Heavy water moderator
10. Pressure tube
11. Steam going to steam turbine
12. Cold water returning from turbine
13. Containment building of reinforced concrete

## Slide 60: Heavy Water Reactors Continued
Fuel | Natural uranium clad in zircaloy
Moderator | Heavy Water
Coolant | Heavy Water
Refueling | On-load

## Slide 61: On-Line Refueling—HWRs
CANDU Reactor

## Slide 62: Countries who operate or used to operate HWRs
Countries that operate HWRs: India, Argentina, Pakistan, Romania, Israel, China, and South Korea, Iran, Canada
Countries that used to operate HWRs: Germany, Sweden, Taiwan, and the United States, Russia, France

## Slide 63: IR-40 Heavy Water Reactor Near Arak, Iran

## Slide 64: Tritium Extraction
Wosong Tritium Removal Facility: ROK Has Produced and Stockpiled Enough Tritium (4 kgs.) to Boost 1,000 Weapons
Some heavy water transmutes into tritium in HWRS.
This tritium must be extracted for safety reasons but can also be used for H-bombs​.

## Slide 65
Plutonium
Neptunium
Fast Neutron Reactions
Thermal Neutron Reactions
Popular neutron moderators include light water, heavy water, and graphite
CONVENTIONAL REACTORS EXPLOIT THERMAL REACTIONS, FAST REACTORS EXPLOIT FAST ONES
Weapons-grade plutonium

## Slide 66: Liquid Metal Fast Breeder Reactor (LMFBR): first reactor to produce electricity
Sodium-Cooled Fast Reactor
Fuel | Pu or MOX- clad in stainless steel
Moderator | None
Coolant | Liquid sodium
Refueling | Off-load

## Slide 67: Liquid Metal Fast Breeder Reactors also have been used to make bomb plutonium
India’s prototype fast breeder reactor under construction at Kalpakkam
Phénix, prototype fast breeder reactor in Marcoule, France – shut down in 2009

## Slide 68: fast breeder reactors are off-line fueled

## Slide 69: Fast Breeder reactor states
Countries that operate FBRs: China, Russia
Countries constructing FBRs: India, China
Countries with plans for FBRs, but not currently operating: Japan, South Korea, France, U.S.
Countries that have had FBRs in the past, but aren’t currently operating: U.S., France, U.K., Germany, Japan
BN-800 reactor at the Beloyarsk Nuclear Power Station in Russia

## Slide 70
Superphenix, France, used to make bombs
Monju, Japan
Kalkar, Germany
Dounrey, UK
Enrico Fermi, Detroit
COMMERCIAL FAST BREEDERS: FAILED & ABANDONED
Clinch River Breeder Reactor

## Slide 71
Fast breeder reactor, India. To be used to make weapons
Fast breeder reactor, Russia. Over budget, completion delayed, tech exported to PRC
First 600 MWe fast breeder reactor, China
Experimental 20 MWe fast breeder reactor, China
Second 600 MWe fast breeder reactor, China
REMAINING BREEDERS: QUESTIONABLE

## Slide 72: Light-Water Reactor (PWR)
Typical Pressurized Water Reactor
Fuel | LEU
Moderator | Light Water
Coolant | Light Water
Refueling | Off-load

## Slide 73: First Light water reactor was designed for submarines

## Slide 74: Three Mile Island Nuclear Power Plant, U.S.

## Slide 75: Light-Water Reactor (BWR)
Typical Boiling-Water Reactor
Fuel | LEU
Moderator | Light Water
Coolant | Light Water
Refueling | Off-load

## Slide 76: Fukushima Daiichi Nuclear Power Plant, Japan

## Slide 77: LWRs are off-load fueled
LWR refueling

## Slide 78: RBMK (Reactor Bolshoy Moshchnosty Kanalny)
Fuel | LEU clad in zircaloy
Moderator | Graphite
Coolant | Light Water
Refueling | On-line

## Slide 79: Chernobyl Nuclear Power Plant, Ukraine

## Slide 80: High Temperature Gas Cooled Reactor
Fuel | Uranium clad in a graphite matrix
Moderator | Graphite
Coolant | Helium
Refueling | Off-load

## Slide 81: Fort St. Vrain Power Station was a one-off
Fort St. Vrain Power Station, HTGR. It operated from 1976 to 1989.

## Slide 82: On-Line Refueling—HTGC (pebble bed)
Under construction in China

## Slide 83: Generation iv Reactors

## Slide 84: Small Modular LWRs

## Slide 85: Fast Small Modular Reactor

## Slide 86: NuScale Reactor

## Slide 87: Summary of reactor characteristics: Magnox Reactor
Example: Chapelcross (UK)
Heat Output: 840 MWt
Electrical Output: 275 MWe
Fuel: Natural Uranium Metal clad in Magnox alloy
Moderator: Graphite
Coolant: Carbon dioxide gas
Refueling: On-load

## Slide 88: Summary of reactor characteristics: High Temperature Gas-Cooled Reactor (HTGR)
Example: Fort St. Vrain
(USA)
Heat Output: 842 MWt
Electrical Output: 330 MWe
Fuel: Uranium carbide particles, enriched, coated in graphite matrix
Moderator: Graphite
Coolant: Helium
Refueling: Off-load

## Slide 89: Summary of reactor characteristics: Pressurized Water Reactor (PWR)
Example: Zion (USA)
Heat Output: 3250 MWt
Electrical Output: 1050 MWe
Fuel: Uranium oxide, 3% enriched, clad in Zirconium
Moderator: Light water
Coolant: Light water
Refueling: Off-load

## Slide 90: Summary of reactor characteristics: Boiling Water Reactor (BWR)
Example: Browne Ferry 2 (USA)
Heat Output: 3293 MWt
Electrical Output: 1065 MWe
Fuel: Uranium oxide, 2.2% enriched, clad in zircaloy
Moderator: Light water
Coolant: Light water
Refueling: Off-load

## Slide 91: Summary of reactor characteristics: Heavy Water Reactor (CANDU)
Example: Pickering (Canada)
Heat Output: 1744 MWt
Electrical Output: 308 MWe
Fuel: Natural uranium oxide clad in zircaloy
Moderator: Heavy Water
Coolant: Heavy water
Refueling: On-load

## Slide 92: Summary of reactor characteristics: Liquid Metal Fast Breeder Reactor (LMFBR)
Example: Phenix (France)
Heat Output: 563 MWt
Electrical Output: 233 MWe
Fuel: Mixed uranium and plutonium oxide (MOX), 20 -27% enrichment, clad in stainless steel
Moderator: None
Coolant: Liquid sodium
Refueling: Off-load

## Slide 93: Summary of reactor characteristics by type
Type of Reactor | Magnox Reactor | High Temperature Gas- Cooled Reactor (HTGR) | Pressurized Water Reactor (PWR) | Boiling Water Reactor (BWR) | Heavy Water Reactor (CANDU) | Liquid Metal Fast Breeder Reactor (LMFBR)
Name of Example | Chapelcross (UK) | Fort St. Vrain (USA) | Zion (USA) | Browne Ferry 2 (USA) | Pickering (Canada) | Phenix (France)
Heat Output | 840 MWt | 842 MWt | 3250 MWt | 3293 MWt | 1744 MWt | 563 MWt
Electrical Output | 275 MWe | 330 MWe | 1050 MWe | 1065 MWe | 308 MWe | 233 MWe
Fuel | Natural Uranium Metal clad in Magnox alloy | Uranium carbide particles, enriched, coated in graphite matrix | Uranium oxide, 3% enriched, clad in Zirconium | Uranium oxide, 2.2% enriched, clad in zircaloy | Natural uranium oxide clad in zircaloy | Mixed uranium and plutonium oxide (MOX), 20 -27% enrichment, clad in stainless steel
Moderator | Graphite | Graphite | Light water | Light water | Heavy Water | None
Coolant | Carbon dioxide gas | Helium | Light water | Light water | Heavy water | Liquid sodium
Refueling | On-load | Off-load | Off-load | Off-load | On-load | Off-load

## Slide 94: Plutonium production by reactor type
Fissile Material Produced by a 1,000 MWe Reactor Operating at 70% Load Factor for One Year |  | 
Reactor Type | Initial Fuel (Enrichment) | Produced Pu (kg)
Light-Water Reactor | U235 (3%) | 175*
High Temperature Gas-Cooled Reactor | U235 (93%) | 29 (plus 64kg U235)
Canadian Deuterium-Uranium (CANDU) | U (natural) | 360
Fast Breeder Reactor | MOX | 300
* For a LWR that has been operating for over 36 months. Note that low-enriched reactors produce more plutonium than high enriched reactors (the fast breeder reactor uses plutonium as fuel, so much of what is produced will actually be reused as fuel). Again, production in a CANDU is the highest for a given power generation. |  | 

## Slide 95: 4. What can be done with spent reactor nuclear fuel?

## Slide 96: Step 6: Spent Fuel Storage

## Slide 97: Commercial Reprocessing: a major undertaking
Rokkasho, Japan: over 20 billion spent, under construction since 1993

## Slide 98
E. ASIA REPROCESSING: A FUTURE HEADACHE
PRC 50 tHM/yr Pilot plant: ~100 bombs worth of plutonium/yr
Possible PRC 800 tHM/yr EDF plant: ~1200+ bombs worth of pu/yr
Japan’s 800 tHM/yr plant: ~1,200+ bombs’ worth pu/yr, to open 2023
ROK Experimental Pyroprocessing Facility, funding frozen
1st PRC 200 tHM/yr plant under construction to be on line by 2025
2nd PRC 200 tHM/yr reprocessing plant to be on line before 2030

## Slide 99: Ferguson Culler Design: Small, cheap, and quick

## Slide 100: Reprocessing steps
Cooling
Head-end treatment
Separation/Extraction
Conversion of plutonium nitrate to plutonium oxide
Storage of radioactive wastes

## Slide 101: cooling
Cooling Pool

## Slide 102: Head-end treatment
Head-End Process

## Slide 103: Separation/extraction
PUREX – Extraction Process
Windscale reprocessing towers

## Slide 104: Reprocessing Pulse Column

## Slide 105: Plutonium Uranium Extraction Plant at Hanford, Washington

## Slide 106: Cooling Pools for Spent Fuel

## Slide 107: Dry cask storage

## Slide 108: Additional Slides

## Slide 109: Critical Masses of Uranium & Plutonium as a Function of Isotopic Mix

## Slide 110: Estimated Yields for Different Bomb Technologies Using LWR Pu
Chart: Estimated yield in kilotons (kt)
| 1945 Tech | 1950 Tech | 1970 Tech
Weapons Grade, 6% 240 Pu content | 13 | 15 | 16
One-cycle LWR Pu, 14% Pu 240 content | 5 | 10 | 12

## Slide 111: IAEA Safeguards guidelines
Direct Use Materials | Significant Quantity
Pu | 8 kg total element (containing less than 80% Pu-238)
U-233 | 8 kg total isotope
HEU | 25 kg contained U-235
Indirect Use Materials | Significant Quantity
LEU (U-235 <20%) | 75 kg contained U-235 (include natural and depleted U)
Thorium | 20 tons total element
Material | Timeliness Goal
Non-irradiated direct use (Pu in fresh fuel) | One Month
Irradiated direct use (e.g. Pu in spent fuel) | Three Months
Indirect use (e.g. LEU) | One Year

## Slide 112: Basic IAEA Safeguards Methods
Example of IAEA Containment
Example of IAEA Surveillance

## Slide 113: Schematic of Fukushima accident

## Slide 114: Pyroprocessing
“South Korea also has advanced reprocessing technology. One professor of nuclear engineering said that "our capabilities when it comes to pyroprocessing, which involves reprocessing by using electolysis, are world-class.”
Chosun Ilbo, February 19, 2016
Planned ROK Pyroprocessing Plant

## Slide 115: Wolsong Heavy Water Reactors
From the four CANDU-6 reactor cores and spent fuel at Wolsong, the RoK could recover 150 kg of lower-burnup fuel-grade plutonium (discharged during the first cycle after start-up—100 to 400 full-power days after start-up) and about 220 kg of higher burnup fuel-grade plutonium that could be used to fabricate more than 50 nuclear warheads with yields exceeding 20 kilotons based on pure fission solid core, levitated core or hollow core designs.

## Slide 116: ROK Has Produced and Stockpiled Enough Tritium (4 kgs.) to Boost 1,000 Weapons
Wosong Tritium Removal Facility

## Slide 117: Too Much Planned Japanese Plutonium for Any Peaceful Purpose
Rokkasho now may open Fall 2022

## Slide 118: Enriching Uranium For What?
Rokkasho Uranium Enrichment Plant
Japan by 2022 could produce up to ~6,400 kg HEU/year or more than 500 bombs worth per year

## Slide 119: Japan Can Master Boosting and More
The National Institute for Fusion Science (NIFS) in Toki
Japan Atomic Energy Agency’s (JAEA) Naka Fusion Institute, Ibaraki Prefecture
As its contribution to the International Thermonuclear Experimental Reactor (ITER) under construction in France, Japan will provide much of the high-tech components and will host an €1 billion materials testing facility – the International Fusion Materials Irradiation Facility (IFMIF).
Naka Fusion Institute, which includes the Tritium Processing Laboratory
National Institute of Fusion Research

## Slide 120: Estimated Warhead Inventories: PRC, US, Russia
Chart: # of Nuclear Warheads
| China | United States | Russia
Strategic (Deployed) | 1590 | 1950
Tactical (Deployed) | 150
Tactical (Storage) | 2000
Reserve | 250 | 2740 | 720
Awaiting Dismantlement | 2340 | 2700
Source: http://www.tandfonline.com/doi/full/10.1080/00963402.2016.1264213 and http://www.tandfonline.com/doi/full/10.1080/00963402.2017.1290375

## Slide 121: What if China Develops Many MIRVs?
According to the Belfer Center’s Hui Zhang, China’s limited fissile material stockpile means that the country does not have the ability to build significantly more warheads without restarting fissile material production.”
BAS March 24, 2015, Tong and Logan

## Slide 122: What About Chinese Tactical Nuclear Weapons?
China developed and tested a neutron bomb in 1988 as a “technological reserve” - Liu Huaqiu, Senior Chinese Nuclear Scientist
Will China need tactical nuclear weapons to counter the U.S., its allies, or Russia?

## Slide 123: Stocks of Highly Enriched Uranium
Chart: Metric Tons of Highly Enriched Uranium
| China | United States | Russia
Military | 16 | 260 | 616
Naval (fresh) | 152 | 20
Naval (spent | 100 | 10
Civilian | 20 | 20
Excess (mostly for blendown) | 63 | 29
(18 tons)
± 4 uncertainty
(599 tons)
(679 tons)
Source: http://fissilematerials.org/library/gfmr13.pdf and http://fissilematerials.org/library/gfmr10.pdf

## Slide 124: Projected PRC Enrichment Surpluses Beyond Power Requirements ~ 1,500 Bombs a Year
China’s has an estimated surplus of ~19,000 kg HEU
232 SWU required to make 1 kg HEU
Conservatively, in 2020, over 2,500 weapons worth for PRC, over 300 for Japan
120,000 SWU required to refuel 1-GWe reactor with LEU annually (66 GWe PRC, 12.5 GWe Japan in 2020)
Hanzhong and Lanzhow

## Slide 125: Projected Uranium Enrichment Surpluses in East Asia
Projected enrichment
supply vs demand until 2035

## Slide 126: Tons of Separated Plutonium
Chart: Metric Tons Separated Plutonium
| China | United States | Russia
Military | 1.8 | 38.3 | 88
Excess military material | 49.3 | 34
Additional strategic stockpile | 6
Civilian stockpile | 49.5
(1.8 tons assumed)
(87.6 tons)
(169.5-185.5 tons)
± 8 tons uncertainty
Source: http://fissilematerials.org/library/gfmr13.pdf and http://fissilematerials.org/library/gfmr10.pdf

## Slide 127: PRC’s Limited Plutonium Production Capacity Is the Bottleneck to Many More Weapons
PRC has only 2 plutonium production reactors
One is being dismantled
One hasn’t operated since the early 1990s
If restarted, the single reactor could produce roughly 300kg of plutonium a year, only enough to make roughly 75 plutonium triggers or bombs.
Jiuquan plutonium production reactor

## Slide 128: PRC’s Most Immediate Alternative Plutonium Production Option: Its Heavy Water Reactors
Two Candu-6 reactors (600 MWe each) at Qinshan
Capable of producing ~650 kilograms of plutonium a year
Sufficient for roughly >100 bombs a year
Source: https://en.wikipedia.org/wiki/CANDU_reactor

## Slide 129: 1987: Reagan Administration Proposed Using WPSS LWR to Make Weapons Plutonium
Source: http://www.historylink.org/index.cfm?DisplayPage=output.cfm&File_Id=5482

## Slide 130
4 kg weapons-grade Pu assumed per bomb based on DOE estimate.
5.2 kg reactor-grade Pu assumed per bomb based on estimate by Richard L. Garwin (see http://fas.org/rlg/980826-pu.htm)
150 kg weapons-grade Pu conservatively assumed per reactor year (see page 64, http://fsi.stanford.edu/sites/default/files/VAF-June.pdf)
250 kg reactor-grade Pu conservatively assumed per reactor year.
HOW MUCH PLUTONIUM COULD A 1 GWE LWR GENERATE/YEAR?
250 kg
10,000 kg
Chart: Pu (kg) produced per year
| 1 AP1000 reactor
Weapons-grade Pu | 150
Reactor-grade Pu | 250

## Slide 131: PRC’s Other Plutonium Production Bottleneck: Lack of a Large, Reliable Reprocessing Plant
China has decommissioned its large military reprocessing plant

## Slide 132: Solution 1: Buy French Reprocessing plant
Presidents Francois Hollande and Xi Jinping
France agrees to build PRC a large commercial reprocessing plant at Jianyuguan
Planned 800 tHM/yr EDF plant: ~1600 bombs worth of pu/yr

## Slide 133: Solution 2: build and operate your own reprocessing plants
China 200 tHM/year reprocessing plant under construction, operational by 2025? 2,000 kgs pu/yr
Images of 50tHM/year Chinese Reprocessing plant at the Jiuquan Atomic Energy Complex, fully operational 2017, 500 kgs pu/yr

## Slide 134
CHINESE FAST REACTORS
China Experimental Fast Reactor, 20 MWe, operational 2010
China Fast Reactor, 600 Mwe (110 wfpu/year), operational 2026?

## Slide 135
EAST ASIAN REPROCESSING PLANTS
50 tHM/yr Pilot plant: ~100 bombs worth of plutonium/yr
Planned 800 tHM/yr EDF plant: ~1600 bombs worth of pu/yr
200 tHM/year plant is now under construction: ~400 bombs worth of pu/yr
800 tHM/yr Rokkasho plant: ~1,600 bombs’ worth pu/yr, 2021 planned opening
ROK Experimental Pyroprocessing Facility